## Slide 1: Review of road design standards and practices.
Paul Disney
Highways, Traffic, and Road Safety Consultant- EASST
13 March 2024
United Nations Economic and Social Commission for Asia and the Pacific
Find us
@EASSTransport

## Slide 2
To review CAREC road design standards and practices,
to identify how road safety might be improved.
My contribution concentrates on technical issues
(rather than institutional responsibilities).
This short presentation summarises my approach.
Project aims and objectives:
13 March 2024

## Slide 3
How to maximise safety is a fundamental and essential consideration for everyone involved in all modes of travel :
13 March 2024

## Slide 4
We all want the same thing: No fatalities or injuries.
The question is how to progress towards/achieve that aim.
13 March 2024

## Slide 5
There are five important topic areas to improve road safety :
13 March 2024
Road infrastructure engineering
Vehicle design engineering.
Road users as people:: Education, road user skills. children, elderly, disabilities, driver training, licensing.
Laws and enforcement–on+off street, Courts, insurance
Emergency services, speed and effectiveness of response to crashes; subsequent medical treatment.

## Slide 6
Road infrastructure engineering
13 March 2024

## Slide 7
Vehicle design, road users as people, laws and enforcement
emergency services :
13 March 2024

## Slide 8
Our project is concerned with the first –
Road infrastructure engineering and design standards.
But all five areas are inter-related.
And the Traffic Police are fundamentally important to our review, because they pick up the pieces on-road, of the consequences of design choices. Sometimes literally bodies.
13 March 2024

## Slide 9
13 March 2024
Assessment of road infrastructure engineering safety divides into:
1. Existing roads
2. Proposed designs of new road projects, large or small

## Slide 10
Existing roads are assessed traditionally by black spot crash data analysis
13 March 2024
Also by Road Safety Inspection (RSI), practical on-site assessment to identify hazardous conditions. RSI does not check compliance with design standards; RSI looks for risks.

## Slide 11
iRAP is a computerised database technique for RSI, which compiles a valuable inventory of road characteristics important for road safety and presents analyses.
13 March 2024

## Slide 12
13 March 2024
Proposed designs are assessed:
- by Road Safety Audit (RSA)
- by Road Safety Impact Assessment (RSIA),
RSIA is valuable at the Feasibility stage, but not widely used or well understood.
(EU2008/96 Road infrastructure safety management and amended by EU2019/1936 provides detailed definitions)

## Slide 13
13 March 2024
Project identification
Feasibility Study assessment, including Design Standards
Preliminary and Final Design proposals
Construction Contract
Operational opening of the road
Management, maintenance, and rehabilitation
Road transport projects develop through a process of:

## Slide 14
Road safety assessment techniques.
When should each technique be used?
Existing roads or new road designs
Existing Feasibility Draft Detailed Construct Post- Post-
Road Study Design Design Construct Opening
-RSIA->
Impact
Assessment
------------------------------------------ RSA ------------ - - - - - - - - - - - - - - - - ->
Audit
------------ RSI ------------> - - - - - - - - - - - - - - - ->
Inspection
-Crash analysis-> - - - - - ->
------------- RS review -------------------------> - - - - - ->

## Slide 15
Design standards are established during the Feasibility Study and used at this stage to estimate project costs.
13 March 2024
These Design Standards – established and agreed in the Feasibility Study - are then applied without question to preparation of the Preliminary and Final Designs.
Last year I was asked to prepare an RSA of a Final Design for Lake Issyk-Kul Ring Rd, financed by Asian Development Bank

## Slide 21
13 March 2024
My RSA Audit Recommendations were:
General Report, including summary of crash data, and discussions with the local Traffic Police,
Tables with General and location-specific Recommendations.
How road safety audit and inspection can make highway engineering designs safer

## Slide 22
13 March 2024
Speed and overtaking management: longitudinal alignment and speed calming features.
On-road cross-sections: median, lanes, shoulders
Roadside safety: edge protection, crash barriers, embankment side slope, Clear Zones and off-road danger
Intersection designs: major/minor, provision of u-turns, signalisation, roundabout, (no project grade separation)
Accessibility and facilities for all road users, pedestrians, children, elderly, disabled, cyclists, small karts, public transport
Serious problem of animals in the roadway
Road signs and markings
My Recommendations were sub-divided into improvements

## Slide 23
13 March 2024
Speed management is fundamental to road safety.
Speed and overtaking management strategy

## Slide 24
Divide the entire length of the project according to the type of frontage development, into “rural”, “suburban”, or “urban” sections, with precise chainages.
Define sub-sections for special design attention: major intersections, schools, markets, hospitals, etc
Define the desirable operating speed for each section.
Define the consequent speed limit, and design speed.
Speed and overtaking management strategy

## Slide 25
rural, 90km/h – except for sub-standard sections.
special attention to control speeds and overtaking at major intersections.
Speed and overtaking management strategy
13 March 2024

## Slide 26
suburban, 60 km/h, typically residential, with access needs, but much less activity.
  classify village bypasses as suburban, usually 1 or 2 junctions with village access roads, also pedestrians and bus stops.
Speed and overtaking management strategy
13 March 2024

## Slide 27
urban and special Low Speed Zones , 40 km/h or 30km/h:
  town centres with retail and business frontages, lots of parking and pedestrian activity.
  special attention to LSZs for schools, markets, hospitals, etc.
Speed and overtaking management strategy

## Slide 28
Introduce simple boundary gateway features between sections with different operating speeds.
To increase driver awareness, coordinate cross-section changes, from rural to suburban to urban shoulders, footways, drainage
Speed and overtaking management strategy
13 March 2024

## Slide 29
Provide repeat speed limit signs as signs, and/or large painted signs on the road surface.
And possibly as interactive signs, which flash when a vehicle is going too fast.
Speed and overtaking management strategy

## Slide 30
Introduce rumble strips and/or speed humps.
Speed and overtaking management strategy

## Slide 31
Provide pedestrian refuge central islands
with raised kerbs, but no zebra markings
13 March 2024

## Slide 32
Provide pedestrian (zebra) crossings
Speed and overtaking management strategy
combined with speed humps,
self-enforcing (reduced Traffic Police speed checks)popular with most people (except speeding drivers)
13 March 2024

## Slide 33
Choice of embankment side slope, and how 1:1.5 directly causes fatalities and serious injuries – ignored by designers?
Criteria for where to provide crash barriers
Choice of drainage ditch profiles
Have Clear Zone criteria been applied? eg trees, utility poles, street lighting poles)
Road Safety Design Decisions

## Slide 34
Design engineers must try to make Clear Zones more “forgiving”, by:
Identifying roadside hazards,
Giving drivers the chance to retain control of steering and speed, and avoid impacts; by, in order:
Eliminating the hazard, or
Moving the hazard, or
Modifying the hazard to make it more “forgiving”, or
Shielding the hazard with crash barriers - the last option.
Road Safety Design Decisions

## Slide 35
Proposed rural simple major/minor t-junction
Intersection designs, and u-turns
central barrier creates need to manage diverted vehicle u-turns
lack of median width for u-turns
high-speed straight through movements in same lane as slow turning vehicles
on this proposal, provision of zebra crossing on 90km/h section

## Slide 36
Rural – proposed larger major/minor X-junction
Accessibility problems, junction design, and u-turns
removes high-speed through movement from turning lane
but lack of median width for safe u-turns
adds crossroad straight-across movement to all other movements
fails to provide any safety for pedestrians or bus stops
13 March 2024

## Slide 37
Proposed simple u-turn arrangement
Intersection designs, and u-turns
same lack of median width for u-turns, which creates a dangerous path for turning vehicles of any size.
Visualise a large truck turning, or agricultural tractor and trailer.
13 March 2024

## Slide 38
Rural – proposed signallisation
Intersection designs, and u-turns
90km/h approaches
no traffic signals provided for side roads
signs and markings not appropriate
13 March 2024

## Slide 39
Urban - proposed major/minor junctions and parking
Intersection designs, and u-turns
Comprehensive review required of design, for 40km/h speed limit, pedestrians, bus stops, freight deliveries, car parking, side road junctions and accessibility
13 March 2024

## Slide 40
Urban - proposed signallisation
Accessibility problems, junction design, and u-turns
13 March 2024

## Slide 41
In addition, other ever-recurring issues:
Crash protection of bridges and culverts, for the structure, against vehicles falling into watercourses, and also for pedestrians from vehicle impacts.
Proposals for underpasses.
Ensuring long-life road paint, and reflectivity of traffic signs
Lack of speed de-restriction signs – so nobody knows where a low speed zone ends?
Where to provide street lighting.
Frangible columns, in particular for street lights, but also for major road signs, and other rigid obstructions
Construction TTM.
How road safety audit and inspection can make highway engineering designs safer
13 March 2024

## Slide 42
Final Design and Contract Documents are finished and agreed, and proposed to ADB for financing
But the Road Safety Audit has identified a lengthy list of Recommendations, most of which require only minor variations to the Final Design,
but would require the designers to spend money and time to change the Design and Contract Documents.
Project experience shows, project after project, that RSA Recommendations are often not even responded to, and when they are, they are dismissed, “buried”, ignored, then conveniently forgotten.
So at this moment in the project:
13 March 2024

## Slide 43
And this “Review of CAREC road design standards and practices” seeks to ensure that road design for road safety is included in the project process from the Beginning, ie the Feasibility stage.
13 March 2024

## Slide 44
We all want the same thing: No fatalities or injuries.
The question is how to progress towards/achieve that aim.
Review of CAREC road design standards and practices

## Slide 45
Thank you!
Paul Disney
Highways, Traffic, and Road Safety Consultant
13 March 2024
Find us
@EASSTransport